## Slide 1
Basic Life Support
Booklet
Royal Site

## Slide 2
Table of Contents
DNAR
Resuscitation Equipment
Anaphylaxis
Strangulation/Ligatures
Paediatric BLS

## Slide 3
DNACPR
Universal Form used in the community setting

## Slide 4
DNACPR
Electronic communication of DNACPR showing red banner to indicate active DNACPR with option to view order in more detail.
Below shows example of expired DNACPR in amber.

## Slide 5
Resuscitation Equipment
Royal Site
Example of a standardised resuscitation trolley on the Royal site. All visible equipment is required to be checked daily. The oxygen cylinder must be at least 3/4 full at all times, to replace the cylinder please contact oxygen porters.
Contents of drawers require a weekly check and drawers should remain tagged in-between.
Please note the 4th drawer needs to be opened first to unlock other drawers.
Replacement equipment for the trolley can be obtained from the resuscitation stock cupboard located on the 9th floor. The key for the cupboard can be signed out from security.

## Slide 6
Royal Suction Device
Example of the electronic suction device at the Royal site.

## Slide 7
Anaphylaxis
In the event of anaphylaxis:
Call 2222 for help
Get anaphylaxis kit located in the 4th drawer of the resus trolley
Follow algorithm ( available in kit)
For further information please access the LUHFT anaphylaxis training module on ESR

## Slide 8
What to do on finding someone who has used a ligature
GET HELP – pull the emergency buzzer and dial 2222 (state medical emergency, confirm your location and request an anaesthetist)
REQUEST the cardiac arrest trolley
SUPPORT the persons weight (if safe to do so)
As soon as possible release the tension on the ligature
Keep the body weight supported or the tension off the ligature until cut
ALWAYS attempt resuscitation in line with trust guidance

## Slide 9
Managing Strangulation
Tuff Cut scissors can be found in all cardiac arrest trolleys acros the organisation, they are located in the airway drawer (Aintree Trolleys – 1st drawer, Royal/BGH Trolleys - 2nd drawer) and should be used for clothing, seat belts & nylon, Leather, Denim, plastic ties and ropes.
Ligature Cutters can be found in all cardiac arrest trolleys across the organisation, they are located in the airway drawer (Aintree Trolleys – 1st drawer, Royal/BGH trolleys 2nd drawer) and should be used for strapping, bubble wrap, tape, rope, some wires, shrink wrap and plastic ties.
For more information please contact: Arran Banks, Deputy Director of Patient Safety arron.banks@liverpoolft.nhs.uk

## Slide 11
Paediatric Basic Life Support

## Slide 12
Paediatric Choking Algorithm

## Slide 13
Management of Choking in an Infant (under 1 year old)
Support the infant in a head-downwards, prone position to enable gravity to assist removal of the foreign body.
A seated or kneeling rescuer should be able to support the infant safely across their lap.
Support the infant’s head by placing the thumb of one hand at the angle of the lower jaw and one or two fingers from the same hand at the same point on the other side of the jaw.
Deliver up to 5 sharp back blows with the heel of one hand in the middle of the back between the shoulder blades.
Do not use abdominal thrusts for infant.

## Slide 14
Management of Choking in Children (over 1 year old)
Back Blows
Back blows are more effective if the child is positioned head down.
Deliver up to 5 sharp back blows with the heel of one hand in the middle of the back between the shoulder blades.
Abdominal Thrusts
Stand or kneel behind the child. Place your arms under the child’s arm and encircle their torso.
Clench your fist and place it between the umbilicus and xiphisternum. Grasp your fist with your other hand and pull sharply inwards and upwards. Repeat up to four more times.

## Slide 15
Paediatric BLS

## Slide 16
Airway Management
Keep airway position neutral for an infant under 1 year old.
In a child over 1 use sniffing position to open airway.

## Slide 17
Chest Compressions
Infant - Use two fingers to deliver chest compressions.
Child over one – Use 1-2 hands to deliver chest compressions